## Slide 1: A risk-based approach for the prioritization of pipe inspections

## Slide 2: The Goal
Pipe Inspections
Degradation State
Maintenance Actions
Identification of an optimal portfolio of pipe inspections for which the
subsequent renovation actions (if necessary) are expected to most improve
the network operability with larger money saving.

## Slide 3: Network Analysis
Large sewerage network in Espoo, Finland
More than 33000 sewer pipes, for a total length of about 900 km.
Pipe inspections are costly.
In this case study, we analyze a subset of selected pipes, whose past inspection results are recorded.

## Slide 4: Methodology Snapshot

## Slide 5: Failure Likelihood
Likelihood
Pipe Features
Local Circumstances
Material
Diameter
Soil
Traffic Load
Pipe Age
Past Events
Blockages
Flushings

## Slide 6: Failure Severity
Class 1
Undoubled pressure pipes from critical pump stations
Main tunnels
Sewer mains and pressure sewers that are within significant groundwater areas
Sewers close to primary or secondary raw water resources
Pipes under railways
Pipes under significant roads
Sewer mains of crucial functional importance for the whole network
Very high pipe-specific flow
Class 2
Sewer mains not included in Class 1
Sewers in protected areas / nature conservation areas
Pipes crossing main water tunnels
Pipes going under a water body (river, lake, sea)
Pipes under buildings
Pipes close to protected ditches
Pipes close to swimming beaches
Pipes other than sewer mains which are within significant groundwater areas
Sewer mains within groundwater areas of less significance
Sewers close to critical underground structures (e.g. subway)
High pipe-specific flow
Class 3
Every remaining pipe

## Slide 7: Risk Assessment

## Slide 8: Decision Tree Analysis

## Slide 9: Expected degradation state

## Slide 10: Expected degradation state

## Slide 11: State probabilities
Given the likelihood interval scores and the likelihood score , the probability of pipe being in state is provided by Bayesian statistics, such that:
Moreover, if we assume uniform distribution within the likelihood interval scores , the probability of pipe of being in degradation state is estimated by:

## Slide 12: Inspection Benefit
The following analysis takes account of the imprecise cost estimates:
disruption cost (direct and indirect)
, renovation costs for each state
inspection cost
The imprecise disruption probability estimates for each degradation state are expressed as

## Slide 13: Inspection Benefit
The expected cost for action on pipe in degradation state is given by:
On the other hand, the expected cost for action on pipe in degradation state is given by:

## Slide 14: Inspection Benefit
Thus, for every possible state we are able to define the optimal decision for pipe by minimizing the expected cost of action . More specifically:
given and .

## Slide 15: Inspection Benefit
The benefit for pipe in state is modeled as a positive interval such that:
After assessing the benefit for every state , the aggregate inspection benefit for pipe is modeled as a weighted sum of the state benefits, whose bounds are:
where .

## Slide 16: Cost efficient inspection portfolios
 | Inspection Benefit | Inspection Cost
Pipe #1 |  | []
… | … | …
Pipe #m |  | []
Synergy #1 |  | []
… | … | …
Synergy #h |  | []
 | Inspection Benefit | Inspection Cost
Pipe #1 |  | 
… | … | …
Pipe #m |  | 
Synergy #1 |  | 
… | … | …
Synergy #h |  | 
Definition of efficient testing portfolios by approximate Robust Portfolio Modeling, taking account of eventual synergies in pipe inspections. By this way, we can employ a benefit-cost analysis in order to define a suitable budget for inspection activities.

## Slide 17: Portfolio Decision Analysis

## Slide 18
Kiitos huomiostanne!
Kysymyksiä?